# Zeiterion Theatre Technical Specifications

# Seating capacity: 1226 – all seating on orchestra level

# Measurements:

Proscenium:	43’ 3’’ wide   x    22’0’’ high

Stage:		26’ 2’’ plaster line to back wall; 4’ 6’’ apron;

84’ 3’’ total width: 12’3’’ stage left wing; 28’9’’ stage right wing

Fly System:	 53’ 9’’ to grid: flyrail elevated 22’0’’ above SL wing

Orchestra Pit:	 43’ 0’’ wide: 4’ 10’’ deep; accommodates approx. 18 musicians

Auditorium:	 100’0’’ to projection booth; 35’0’’ to box booms; 40’0’’ to FOH lighting beam.

Loading Door:	8’0’’ wide  x  12’0’’ high; load into SR wing at truckbed level.

# Dressing Rooms:

Star Dressing Room:    Capacity –   3; Located Substage

Female Chorus Room: Capacity – 20; Located Substage

Male Chorus Room:    Capacity – 20; Located Substage

Principal Dressing	 Capacity  - 5; Located Mezzanine level off stage left (no shower) All dressing rooms are heated/air-conditioned with lighted mirrors, counters, hanging space, bathroom facilities, and showers.(except for principal)

# Audio System:

# House Mixer:		Crest X8HS; 40 inputs; 8Aux Sends			.

Snake:			20 Channels SL, 20 Channels SR

Speakers: 		2 Bose 9702 mid/high Loudspeaker

2 Bose 502  BEX Low

AMPS:			4- Crown K2

Stage Monitors:	4 – RadianRPX112 P/B floor wedges

Microphones:		Call

A 12 station Clear Com system is installed at all necessary

locations.  There are 7 working headsets available for use.

# Rigging System:

36 linesets: double purchase: 1 ½’’ I.D. 50’0’’ long pipes

(Location See Attached Sheet)

# Stage Draperies:

Red Velour main curtain – flys and travels; red velour legs and border;

4 sets of black velour legs – 30’0’’ high by 12’0’’ wide;

4 black velour borders – 50’00 wide  x  14’0’’ high;

full stage black velour backdrop – 30’0’’  x  50’0’’ wide;

sky blue scrim – 30’0’’ high  x  50’00’’;

silver/gray traveler/fly at midstage.

# Lighting System:

Control Board:	ETC Express 125

Dimming:	57 – 2.4K and 11 – 6.2 K TTI Dimmers

Positions:	FOH Beam (24 permanent 575w, ETC Source 4 26Deg), SL & SR Box Booms (8 straight hung 575w ETC Source 4 in each), 4 Overhead Electrics, and Stage Booms.

Follow Spots:	2 – Xenon Troupers

Power Tie In:	400 Amp, 3 Phase, 120/208 Volt located SR-50’0’’ from Center

Units Available:		24: ETC Source 4  575 w26Deg. Located on stage

24: ETC Source 4  575 w36Deg. Located on stage

36:   Altman Par 64 500 W MED Located on stage

6:   8’’  1000w fresnel on stage

12: 6’’    400w  fresnel on stage

8:  3 circuit 300w strips w/ rondels

colored red, blue, and amber